## Slide 1: The 4rd MCX Training Workshop
Associate Professor
Dept. of Bioengineering
Northeastern University, USA
Qianqian Fang, PhD
MCX website: http://mcx.space
MCX’22, Boston

## Slide 2: Preparation
Download packages matching your OS from:
http://mcx.space/nightly/release/MCX22
allinone packages works for all platforms)
Windows users: please download and install the installer and run it using Administrator account; run MCX Studio with Administrator account for the 1st time, follow prompt
MATLAB setup: open MATLAB, run
  edit(fullfile(userpath,'startup.m’))
  add addpath(‘/path/to/toolbox’) to each of the matlab toolboxes
  Save and restart MATLAB (Windows user only needs to add iso2mesh/brain2mesh)
To test:
  Start MATLAB, type “which mcx mmc mcxcl s2m”, see output
  In matlab, run mcxlabcl(‘gpuinfo’) should print GPU/CPU info

## Slide 3: Outline
Introduction
MCX training
Iso2Mesh/Brain2Mesh training
MMCLAB training
Edward Xu
Rahul Ragunathan

## Slide 4: Introduction
MCX website: http://mcx.space
MCX’22
Session 1.A

## Slide 5: MCX Suite – full-stack solution
MCX
MCX-CL
MMC
(Trinity)
Iso2Mesh
Standalone
Mex files
MATLAB
GNU Octave
GUI
MCXLAB/CL
MMCLAB
MMC-SSE/CL/CUDA
MCX Cloud
Brain2mesh
pymcx

## Slide 6: Why MCX/MMC matters to fNIRS users
Tran AP+, Yan S+, Fang Q*, (2020) “Improving model-based fNIRS analysis using mesh-based anatomical and light-transport models," Neurophotonics, 7(1), 015008

## Slide 7: Mini-Course Outline
Package name | Utility name
MCX | MCX Cloud
 | MCXLAB
Iso2Mesh | Mesh generation
 | Brain meshing
MMC | MMCLAB
Hands-on | 

## Slide 8: Acknowledgement
This project is funded by the NIH/NIGMS under the grant R01-GM114365 (MCX, http://mcx.space)
and NIH/NINDS under grant U24-NS124027 (https://neurojson.org).

## Slide 9: Hardware Recommendations
MCX website: http://mcx.space
MCX’22
Session 1.B

## Slide 10: Recommended Hardware
The more cores, the merrier! Use many consumer-grade cards together!
MCX (CUDA) is NVIDIA GPU only; MCXCL/MMCL can run on (almost) all processors. But CUDA is faster than OpenCL.
MCX uses single-precision floating-point operations, Tesla cards (more expensive) are not necessarily faster.
Dedicated GPU preferred – i.e. not used for display. Multiple-cards can gain speed almost linearly.
MCX
MCX-CL
MMC
Fiji, Polaris,Vega,
Navi

## Slide 11: GPU Benchmarks/Contest
http://mcx.space/gpubench

## Slide 12: MCX1

## Slide 13: MCX input/output
MCX website: http://mcx.space
MCX’22
Session 1.C

## Slide 14: MCX/MMC Algorithm Diagram
Launch (p, v, w)
Determine unitless
scattering len. S
N photon?
End
Calculate the distance D to cell boundary, define d=min(D, S/µs)
Move photon by d: p= p+d*c
S=S-d*µs
Accumulate Δw to the cell enclosing the path
Cross a boundary & n1≠n2?
Arrive at a scattering site (S≤0)?
Do Reflection?
Reflect
Transmit
Determine new
Scattering dir: v
Time limit exceeds?
Exit domain?
n
y
y
n
n
y
y
n
n
y
y
n
Update packet weight Δw=w*[1-exp(-µad)]
w=w-Δw
Start

## Slide 15: Supported Source Types
Point sources:
  Pencil beam, isotropic source, cone beam
Line sources:
  Isotropic line source, slit source
Area sources:
  Planar, disk, Fourier domain source, Gaussian source, arbitrary 2D pattern source (load a 2D array)
All area/line sources support convergent and divergent beams (cfg.srcdir=[vx, vy, vz, focal_length])
p0
v0
p0
v0
focal_length
(negative)

## Slide 16: MCX inputs and outputs
Input data types:
  Optical parameters: tissue volume, μa/μs/g/n, source/detectors, time-gate settings
  MC configurations: seeds, photon num, normalization, …
  GPU configurations: thread#, block#, which GPU …
Input format:
  JSON file (for standalone MCX/MCXCL)
  cfg-struct in MATLAB (MCXLAB)
  cfg-dict in pymcx
Output:
  Volumetric output: fluence, energy deposition, Jacobians
  Detected photon output: partial-path, partial scattering
  Trajectories: (use for debugging purposes only, do not recommend for data processing)

## Slide 17: Photon detection and partial path lengths
MCX/MMC detectors are defined by a spherical shell intersect with the tissue boundary.
Detection only happens when a photon escape from “domain” to “background” (0-voxels or out-of-bounding-box in MCX)
For any detected photon: total pathlength L is a sum of the cumulative pathlength in each tissue type
= PPL1 + PPL2 + PPL3
User-customizable output (--savedetflag/-w ‘DSPMXVW’)
  D – output detector ID (detps.detid)
  S – partial-scattering event counts (detps.nscat)
  P – partial-pathlengths (detps.ppath)
  M – (partial) momentum transfer (detps.mom)
  X – exit photon positions (detps.p)
  V – exit photon directions (detps.v)
  W – initial packet weight (detps.w0)
tissue#1
tissue#2
tissue#3
src
det

## Slide 18: MCX Cloud Demo
MCX website: http://mcx.space
MCX’22
Session 1.D

## Slide 19: MCX Cloud – an in-browser cloud-based MC simulator

## Slide 20: Demo 1
Built-in examples (widefield)
  Load
  Preview
  Run
  Download
  Edit
  Share
  Hands-on
    Change source type
    Change media optical properties

## Slide 21: Demo 2
Design new simulation
  Add absorber
  Add detector
  Load output data
Hands-on experiment:
  Define a 4-layer medium (10^6 photon)
1. Skin and skull | 0.019 | 7.0 | 0.89 | 1.37
2. CSF | 0.004 | 0.009 | 0.89 | 1.37
3. Gray matter | 0.02 | 9.0 | 0.89 | 1.37
4. White matter | 0.08 | 40.9 | 0.84 | 1.37
1. Skin and skull |  |  | 0.89 | 1.37
2. CSF |  |  | 0.89 | 1.37
3. Gray matter |  |  | 0.89 | 1.37
4. White matter |  |  | 0.84 | 1.37

## Slide 22: MCXLAB
MCX website: http://mcx.space
MCX’22
Session 1.E

## Slide 23: Before we get started…
Important
Open MATLAB, and cd the root folder of MCXStudio, and run a script named mcxsuite_addpath.m
Please type USE_MCXCL=1; in MATLAB’s Command Window if you do not have NVIDIA graphic card. You need to re-define this line after you type “clear” or “clear all”. To test if your GPU is recognized by MATLAB:
Please type info=mcxlab(‘gpuinfo’) in MATLAB to check your GPU information.
All demo scripts can be found under USB Folder: Presentations\3_MCXLAB_Demo\

## Slide 24: MCX vs. MCXLAB
Inputs
Outputs
MCX
MCXLAB
cfg.
nphoton
vol
prop
srcpos
srcdir
tstart
tend
tstep
Structure
Outputs
.inp
.json
.vol
.nii/.jnii/.mc2 (fluence)
.jdat/.mch
(detected photon)
vol.nii
(masked volume)
fluence
detpho-tons
vol
OR
Notes: Mapping between MCX and MCXLAB

## Slide 25: Input & output
Input
nphoton
vol
prop
tstart
tend
srcpos
srcdir
tstep
Output
fluence
detphoton
vol
trajectory
cfg
detpos
Fluence generation
Source-detector pair
Optional

## Slide 26: Demo 1: A basic MCXLAB simulation
Photon count
Define volume
Source position
Source direction
Optical properties for different tissue type
Time gate design
Run MCXLAB
MCXLAB can be run with a very short script
See Presentations/3_MCXLAB_Demo/demo1.m

## Slide 27: Extended Example 2: A 3-D brain simulation
Exercise Goals:
Create a simulation using a complex segmented brain
Understand the output quantities
Action Item:
Please load in MATLAB the below script
Presentations/3_MCXLAB_Demo/Brain_mcxlab_demo.m

## Slide 28: Extended Example 2: A 3-D brain simulation
Simulation of light propagation in realistic brain
The brain slices at 2 ns
Light propagation in brain ()
Source position: [87 85 204]
Source direction: [0 0 -1]
Number | Property
0 | Background
1 | Gray matter
2 | White matter
3 | CSF
4 | Bone
5 | Scalp
See Presentations/3_MCXLAB_Demo/Brain_mcxlab_demo.m

## Slide 29: Iso2Mesh
MCX website: http://mcx.space
MCX’22
Session 2.A

## Slide 30: How to define a mesh?
Point cloud Triangular surfaces Tetrahedral elem.
(node) (face) (elem)
node=
[
x1,y1,z1
x2,y2,z2
x3,y3,z3
…
]
face=
[
n11,n12,n13 <,label1>
n21,n22,n23 <,label2>
…
]
elem=
[
e11,e12,e13,e14 <,label1>
e21,e22,e23,e24 <,label2>
…
]
May have an extra column for labels

## Slide 31: Mesh-based Monte Carlo (MMC) – when you should consider it?
Pros
    “Highest” accuracy when modeling light in curved shapes
    Memory-efficient – small memory footprint
    Important when dealing with a thin-layer of high-contrast medium
    Important when dealing with complex refractive index mismatched boundaries
Cons
    Needs pre-processing – mesh generation to model complex shapes
    Needs post-processing – interpolation in the mesh space to create plots

## Slide 32: Advantages of Iso2Mesh
  Designed for simplicity – a “one-liner” mesh-generator
  Highly modularized
  Cross-platform (Linux, Windows, Mac)
  Matlab(7.0+)/Octave(3.0+) compatible
  Fast; fine-grained granularity
  Build on open-source software
  Free and open-source
  New: easy-to-use GUI: img2mesh/i2m
  New: JSON/JMesh unified mesh storage format
CGAL
Tetgen
JMeshLib
http://jmeshlib.sf.net
http://tetgen.berlios.de/
http://www.cgal.org
Cork
https://github.com/gilbo/cork

## Slide 33: Iso2Mesh Workflow Overview
Simple shapes
Volumetric images (gray-scale, multi-label)
Surface meshes
Tetrahedral meshes
v2s , vol2surf
v2m , vol2mesh
s2m , surf2mesh
volface
s2v, surf2vol
m2v, mesh2vol
Smoothing
Boolean
Repairing
Down-sample
Refining
Plotting

## Slide 34: i2m (img2mesh) GUI
MCX website: http://mcx.space
MCX’22
Session 2.B

## Slide 35: Introducing Img2Mesh (i2m)
An intuitive step-by-step meshing software
Graph-based data organization
To start: type i2m and press enter in MATLAB

## Slide 36: Demo 1: img2mesh (i2m) GUI
Task 1:
  Create a cube (two corners from [0,0,0] to [60, 60, 60]) and a sphere (O:[30 30 30], R:20) surface
  Merge the two surfaces
  Create volumetric mesh
Task 2:
  Create a lattice (x: [0,100],y:[0,100],z:[0,20,100])
  Mesh the lattice (surface to mesh)
  Create a cylinder (axis from[-1,50,50] to [101,50,50], R:10)
  Surface Boolean (‘first’) the two surfaces
  Create volumetric mesh

## Slide 37: Demo 2 – cgalmesh: direct conversion from a segmented volume to a mesh
Exercise Goals:
Try the fully automated meshing pipeline v2m(‘cgalmesh’)
Understand how to control mesh density
Action Item:
Please load in MATLAB the below script
Presentations/5_Iso2Mesh_Demo/Demo2_v2m_cgalmesh.m

## Slide 38: Demo 3: A brain mesh from segmentation
Open iso2mesh/sample/brain_seg.tif using
    cd([fileparts(which('s2m')) filesep 'sample’])
    fprintf(1,'loading segmented brain image...\n'); for i=1:256 brain(:,:,i)=imread('brain_seg.tif',i); end brain=uint8(brain);
Mesh the volume using
  [node,elem,face]=v2m(brain,[],20,100,'cgalmesh');
Visualize a particular label, or cross-section using plotmesh
Irregular bumps affecting smoothness
Gyrications are lacking

## Slide 39: Brain2Mesh
MCX website: http://mcx.space
MCX’22
Session 2.C

## Slide 40: Demo 1: CGALMesh from SPM Tissue probability maps
filename = 'ANTS17-0Years_head.nii';
for i = 1:6
A= load_nii(sprintf('datasets/1/c%i%s',i,filename));
seg(:,:,:,i) = A.img;
end
[~,I] = max(seg,[],4);
I(:,:,1:70,:) =0;
I(I==6)=0;
opt.radbound = 2; opt.distbound = 2;
[node,elem,face] = v2m(uint8(I),[],opt,50,'cgalmesh');
Reading in data and storing into 4D array
Find indices with max probability
Removing background and non-brain related areas
Irregular bumps affecting smoothness
Gyrications are lacking
opt.radbound: facet size (max radius of Delaunay sphere)
opt.distbound: maximum deviation from specified isosurfaces
maxvol: value or array containing the maximum allowed element size for the whole mesh or label, respectively

## Slide 41: Demo 2 (a,b): Surface-based meshing using volumetric data: Brain2mesh
Exercise Goals:
Generate volumetric mesh from SPM Tissue probability maps using “Brain2mesh”
Action Item:
Please load in MATLAB the below script
Presentations/6_Brain2Mesh_Demo/example_2a_SPM.m
Notes: Discrepancies in fluence contour plots;
Demo_1_meshvsvoxel_reflection;

## Slide 42
Demo 2a: Surface-based meshing using volumetric data, SPM Dataset
data = loadnifti('datasets/1/c2ANTS17-0Years_head.nii.gz');
seg.wm = data.img;
data = loadnifti('datasets/1/c1ANTS17-0Years_head.nii.gz');
seg.gm = data.img;
data = loadnifti('datasets/1/c3ANTS17-0Years_head.nii.gz');
seg.csf = data.img;
data = loadnifti('datasets/1/c4ANTS17-0Years_head.nii.gz');
seg.skull = data.img;
data = loadnifti('datasets/1/c5ANTS17-0Years_head.nii.gz');
seg.scalp = data.img;
[node,elem,face] = brain2mesh(seg);
Output labels:
0. Background/air
1. Scalp
2. Skull
3. CSF
4. GM
5. WM

## Slide 43
Demo 2b: Surface-based meshing using volumetric data, Colin27 Dataset
tissues = {'FAT','FAT2','GM','MARROW','SKIN-MUSCLES','SKULL','VESSELS',...
'WM','CSF','MUSCLES','DURA'};
for i = 1:length(tissues)
data(i) = loadnifti('datasets/2b/%s.nii.gz',tissues{i}));
data(i).img = mat2gray(data(i).img);
end
seg.wm = data(8).img; %WM
seg.gm = data(3).img; %GM
seg.csf = data(9).img + data(7).img + data(11).img; % CSF + Vessels
seg.skull = data(6).img + data(4).img; % Skull + Marrow
seg.scalp = data(5).img + data(10).img + data(1).img + data(2).img; %Skin-muscles + muscles + fat/fat2
cfg.radbound.wm = 3.4;
cfg.radbound.gm = 3.4;
cfg.radbound.csf = 4;
cfg.radbound.skull = 5;
cfg.radbound.scalp = 6;
cfg.maxvol = 100;
[node,elem,face] = brain2mesh(seg,cfg);

## Slide 44: brain1020 –10-20/10/5 points
landmarks=brain1020(node, headsurf)
lm2=brain1020(node, surf, lm1, 10, 5)

## Slide 45: MMCLAB
MCX website: http://mcx.space
MCX’22
Session 3.A

## Slide 46: Demo 1: A basic MMCLAB simulation
Exercise Goals:
Explain line-by-line the essential elements to define a basic MMCLAB simulation
Understand how to visualize and interpret output such as light fluence and detected photon information
Action Item:
Please load in MATLAB the below script
Presentations/7_MMCLAB_Demo/demo1.m

## Slide 47: Demo1 (MMCLAB Basics)
Similar configurations as MCXLAB, see comparison http://bit.ly/2K0rG4R
Generate Mesh and Assign optical properties
Configure source (can be non-collimated), detectors
Configure time gates
Other essential information
  Photon counts (nphoton)
  RNG seed (-1 for total random)
  Other optional information
  Exit information (issaveexit)
  Seed information (issaveseed)
  …
demo1.m

## Slide 48: Demo1 (MMCLAB Basics)
Almost the same output as MCXLAB
Fluence
Detected photons
  Detector ID
  Scattering Events (each medium)
  Path Length (each medium)
  Position & Direction (issaveexit=1)
  Initial (and final) photon weight
Seeds
Two functions
mmcdetweight
mmcdettime
Fluence Distribution
TPSF on Detector
demo1.m

## Slide 49: Demo 2: Wide-field MMC
Exercise Goals:
Understand how to define external wide field source and detector in MMCLAB
Action Item:
Please load in MATLAB the below script
Presentations/7_MMCLAB_Demo/demo2.m
Two functions
mmcaddsrc
mmcadddet

## Slide 50: Demo 2 (Wide-field MMC)
demo2.m
merge source domain
merge detector domain
run MMC, plot results
on original mesh